## Slide 1
MAC Layer Protocols for Wireless Networks

## Slide 2
Interference / Collisions
Interference on node b
(“Hidden terminal problem”)
a
b
c
a
b
a
b
c
d
Interference on node b
a and b interfere and hear noise only
Packets which suffered collisions should be re-sent.
Ideally, we would want all packets to be sent collision-free, only once…

## Slide 3
Contention-based protocols
  CSMA — Carrier Sense Multiple Access
    Ethernet (CSMA/CD) is not enough for wireless (collision at receiver cannot detect at sender)
CSMA Protocol
A
B
C
Hidden terminal: A is hidden from C’s CS

## Slide 4
Hidden Terminal Problem
A and C want to send data to B
  A senses medium idle and sends data
  C senses medium idle and sends data
  Collision occurs at B
A
B
C
Data
Data

## Slide 5
Collision Avoidance w/ RTS/CTS
A and C want to send to B
  A sends RTS (Request To Send) to B
  B sends CTS (Clear To Send) to A C “overhears” CTS from B
  C waits for duration of A’s transmission
A
B
C
1.RTS
2.CTS
2.CTS
3.Data

## Slide 6
Overview of MAC Protocols
Contention-based protocols (contd.)
  IEEE 802.11 Distributed Coordination Function (DCF)
    Based on CSMA/CA

## Slide 7
802.11 DCF (Distributed Coordinate Function)
Station listens before transmission
If medium is free for more than DIFS: transmits
Otherwise, uses exponential backoff mechanism

## Slide 8
IEEE 802.11 DCF
Distributed coordinate function: ad hoc mode
  In a network where a number of stations contend for the wireless medium, if multiple stations sense the channel busy and defer their access, they will also virtually simultaneously find that the channel is released and then try to seize the channel. As a result, collisions may occur.

## Slide 9
IEEE 802.11 DCF
In order to avoid such collisions, DCF also specifies random backoff, which forces a station to defer its access to the channel for an extra period. The length of the backoff period is determined by the following equation:
B a c k o f f T i m e = r a n d o m ( ) × a S l o t T i m e

## Slide 10
Random Backoff
Pick a timeslot chosen uniformly in [0, CW]
Listen up to chosen slot
  Transmit if nobody else started transmitting
  Wait if somebody else started transmitting
Time

## Slide 11
Example: A Successful Transmission
A and B happened to choose different slots
  Node A chooses slot 4, hears nothing, transmits
  Node B chooses slot 8, hears Node A,
Success: exactly one node in first non-vacant slot
Node A:
Node B:
Slot choice (slot #4)
Slot choice (slot #8)
Time

## Slide 12
Example: A Collision
A and B happened to choose slot 4
  Both listen and hear nothing
  Both transmit simultaneously
Collision: ≥ 2 nodes in first non-vacant slot
Node A:
Node B:
Slot choice (slot #4)
Slot choice (slot #4)
Time

## Slide 13
High Contention Causes Collisions in CSMA
Uniform distribution “fills up,” quickly
Unacceptable collision rate above
~15 transmitting sensors